## Slide 1
  Structural calculation of pipe rehabilitations according to the DWA-A 143-2
  Dipl.-Ing. (Univ. Belgrade) Vladimir Lacmanovic

## Slide 2: Agenda
Basics for the structural calculation of buried pipes A 127
Basics for the structural calculation of Liners A 143-2
Verifications and proofs of Liners according to A 143-2
Software IngSoft EasyPipe
Examples (Live)
FEM Analysis

## Slide 3
ATV-DVWK-A 127 standard - abstract
Structural calculation of buried pipes

## Slide 4: Pipe-Soil-System
ATV-DVWK-A 127 standard
Air
Soil

## Slide 5: Soil
Great importance for structural calculation
For a solid rock, the pipe only prevents leakage (solid rock is self-supported)
Poor soil in bedding zone combined with great coverage or heavy traffic breaks the strongest pipe
Soil types according to ATV-DVWK-A 127
Soil zones around pipe and Young’s modulus accordingly
Assumption of consolidated soil in DWA-A143-2 E1 = E2 = E3 = E4
ATV-DVWK-A 127 standard

## Slide 6: Rigid Pipe-Soil-System
System stiffness VRB
  VRB = SR / SBh
  Rigid pipe
  VRB > 1  rigid Pipe-Soil-System
Concentration factor lR
  Depends on bedding, stiffness ratio etc.
Concrete, reinforced concrete and stoneware pipes always result in a rigid Pipe-Soil-System
Rigidity of the Pipe-Soil-System of thermoplastic, duroplastic and even metal pipes depend on the system stiffness
ATV-DVWK-A 127 standard
Notes: Animation
Mineralwolle auf Tafel einzeichnen
Einfeldträger mit Feder auf Tafel zeichnen: Höhere Verdichtung im Bereich E1 (Überschüttung) ist ungünstig(er) für das Rohr

## Slide 7: Flexible Pipe-Soil-System
System stiffness VRB
  VRB = SR / SBh
  Flexible pipe
  VRB ≤ 1  flexible Pipe-Soil-System
Concentration factor lR
  Depends on bedding, stiffness ratio etc.
The pipe deforms enough to transmit the greater part of the loads on the nearby soil but only in the usability tolerance limits
ATV-DVWK-A 127 standard
Notes: Animation
Mineralwolle auf Tafel einzeichnen
Einfeldträger mit Feder auf Tafel zeichnen: Höhere Verdichtung im Bereich E1 (Überschüttung) ist ungünstig(er) für das Rohr

## Slide 8
Theory
Basics for the structural calculation of Liners
DWA-A 143-2

## Slide 9: DWA-A 143-2
A 143-2
Semi-probabilistic concept
Three (+1) host pipe conditions
Traffic loads: LM1, LM71 etc.
Interaction proof
Shear proof
Dynamic proof
Theory DWA-A 143-2

## Slide 10: General design form
Stresses
  SD Design value of the influences SD = Σ (Influences x Partial safety factors γF)
  RD Design value of the material resistance RD = Material strength / Partial safety factor for the specific material γM
Deformations
  are limited to 10 % total (elastic + imperfections)
  Elastic deformations are limited to
    δv,el ≤ 3 % for the water pressure due to groundwater
    δv,el ≤ 6 % for earth and traffic loads
    δv,el ≤ 2 % or 10 mm in German railway (DB) inner pressure area
Theory DWA-A 143-2

## Slide 11: Semi-probabilistic Concept in A143-2
… semi-probabilistic concept in the DWA-A 143-2 leaning on Eurocodes with:
Partial safety coefficients γF for influences
  Permanent loads (Dead load, Earth loads, Surface loads, etc.) γF = 1.35
  Variable loads (Traffic loads except road traffic load, Groundwater) γF = 1.50
  Road traffic loads γF = 1.35
  Short term floodwater γF = 1.10
  Internal pressure (including pressure surge) γF = 1.50
  Inspection pressure γF = 1.20
  Temperature change γF = 1.10
  Imposed deformations γF = 1.10
Theory DWA-A 143-2

## Slide 12: Semi-probabilistic Concept in A143-2
Semi-probabilistic concept in the DWA-A 143-2 leaning on Eurocodes with:
Partial safety coefficients γM for material resistance
  Plastic liners, hardened on site γM = 1.35
  Pre-fabricated plastic liners (Extrusion or similar) γM = 1.25
  Cement liner γM = 1.50
  Stainless steel γM = 1.15
  Resistance with a favorable effect (e.g. Imposed liner deformations at HPC III) γM = 1.00
  Concrete and vitrified clay host pipes for the proof of pressure zones (eq. 102) γM = 1.50
Coefficients for combinations ψ
  Temperature change combined with groundwater ψ = 0.7
  Actual groundwater combined with earth and traffic loads ψ = 0.9
  Replacement load for groundwater combined with earth and traffic loads ψ = 0.7
Theory DWA-A 143-2

## Slide 13: Host Pipe Condition I
Host pipe alone is capable of bearing loads
  Leaks in connections
  no cracks (only capillary cracks)
Imperfections
  Local imperfection
  Annular gap
Influence
  Outer pressure due to groundwater
Required proofs
  Stresses and deformations
  Buckling (Stability)
Theory DWA-A 143-2

## Slide 14: Host Pipe Condition II
Host pipe-soil system is capable of bearing loads
  Longitudinal cracks, minor pipe deformation δV < 6 %
  Functionality of the lateral bedding proven through soil boring
Imperfections
  Local imperfection
  Annular gap
  Ovalization
Influence
  Outer pressure due to groundwater
Required proofs
  Stresses and deformations Buckling (Stability)
Theory DWA-A 143-2

## Slide 15: Host Pipe Condition III
Host pipe-soil system no longer capable of bearing loads in the long-run
  longitudinal cracks, significant pipe deformation δV ≥ 6 %
  In addition to HPC II liner takes up earth and traffic loads
Imperfections
  Local imperfection
  Annular gap
  Ovalization
Influence
  Outer pressure due to groundwater
  Earth and traffic loads
Required proofs
  Stresses (in host pipe as well), deformations, Buckling (Stability)
  Interaction (superposition or combined on the same system)
Theory DWA-A 143-2

## Slide 16: Host Pipe Condition IIIa (informative only )
As HPC III however
  the load transmission in the host pipe pressure zones is not possible due to insufficient strength of host pipe material
  Pressure transmission in the springlines not possible
  host pipe is cracked in fragments not in four joints
  HPC IIIa has an informative character only and finds place in appendix K of the DWA-A 143 part 2
  Liner is calculated as buried pipe (elastically bedded ring) according to the ATV-DVWK-A 127
  Host pipe is regarded as “gravel”
Theory DWA-A 143-2

## Slide 17: Host pipe condition II or III?
Theory DWA-A 143-2
 | Determination point | HPC II | HPC III
1 | Ovalization ωGR,V | ≤ 6 % | > 6 %
2 | Cover depth h | High | Low1
3 | Traffic load influence | Low | High
4 | Load increase in time (foundations, surface load) | No | Yes
5 | Plaster marks are opening | No | Yes
6 | Proof qv,d / krit qv,d (according to the appendix F) | ≤ 1 | > 1
7 | Cavity formation in soil due to infiltration | No | Yes
8 | HP-Soil-System with Liner under hW displaceable | Yes | No
1) Note: cover depth h < 1m and h < da for road traffic loads h < 1.5 m under railway loads |  |  | 

## Slide 18: Imperfections circular shape
Local imperfection
  Consider deformations in the host pipe during the installation of the liner as well as the abbreviation from the planned trace
  Consider structural imperfections (local decrease of stiffness and/or wall-thickness)
  Is required in the calculation to trigger the decisive buckling case
Ovalization
  Is the form that host pipe takes after its cracked in crown, invert and springlines
Annular gap
  Occurs through shrinking of the resin in the liner or shrinking of the filling material
Theory DWA-A 143-2

## Slide 19: Imperfections
Egg-shaped profile
  Four joint deformation inwards
  HPC II and III
  Local imperfection results as
  ωL = ωL + ωGRV/10 = (0,5% + 3,0%/10) x rK = 0.8% rK
Imperfections are defined more precisely in the DWA-A 143-2 dependent on:
  Installation method
  Load case and HPC I – II – III
  Profile geometry
Theory DWA-A 143-2

## Slide 20: Minimal required imperfections
Method | Hose | Back-formed | Single pipe | Wounded without gap | Wounded | Pinched
Local imperfection | ≥ 2% | ≥ 2% | ≥ 1% | ≥ 1,5% | ≥ 1% | ≥ 2%
Ovalization (II,III) | ≥ 3% | ≥ 3% | 0% | ≥ 3% | 0% | ≥ 3%
Gap | ≥ 0,5% | ≥ 2% | ≥ 1-2 mm | ≥ 2 | Material dependent | ≥ 0.12%
Theory DWA-A 143-2
Circular liner geometry
Egg-shaped liner geometry
 | Non masoned host pipe | Masoned host pipe
Local imperfection | ≥ 0,5% (rK) +ωgrv/10 | ≥ 1% (rK) + ωgrv/10
Ovalization (II,III) | ≥ 3% (crown radius) | 
Gap | ≥ 0,4% | 

## Slide 21: Eccentricity
HPC III
Distance of the rotation point (crown joint) to the mid-axis (the better the host pipe, the higher the value)
Input in % of the host pipe thickness
Normal HP state eG= 0,35
Theory DWA-A 143-2

## Slide 22: Loads
Load | HPC I | HPC II | HPC III
Self-load | X | X | X
Temperature difference | X | X | X
Water pressure due to groundwater | X | X | X
Inner pressure | X | X | X
Earth load |  |  | X
Traffic load |  |  | X
Theory DWA-A 143-2

## Slide 23: Road Traffic Loads
Load model 1 according to DIN EN 1991-2 replaces the Street loads HGV 60, HGV 30 and Truck 12
Ground stresses due to road traffic loads in a diagram form depending on
  Host pipe length
  Cover depth (0.5 – 10 m)
  Diameter
All diagrams and formulas for α = 0.8, it supposed to be calculated with 1.0 (German NA for EC 1-2)
Dynamic proof required for cover depths hE < 1.5 m
Theory DWA-A 143-2

## Slide 24: Railway Traffic Loads
Installation with earth cover less than 1.1m allowed only with special permission
Railway load in shallow depth can be distributed according to DIN EN 1991-2
Dynamic proof required for up to 5.5m depth
Theory DWA-A 143-2

## Slide 25
IngSoft EasyPipe and DWA-A 143-2
Verifications and proofs

## Slide 26: Verification concept in the A 143-2
  Cross-sectional forces and stresses
  Stability
  Inner pressure, temperature
  Deformations (Service load)
  Soil limit stress (Service load)
  Stress in the host pipe
Verifications and proofs

## Slide 27: Cross-sectional forces and stresses
Factors for cross-sectional forces
  For HPC I and II (attachment D), circular and egg-shape geometry
  For HPC III (attachment E), circular geometry only
Stress inner and outer fibres
  αki and αka correction factors ovality
Shear stress
  Shear strength required, BÜV-recommendation max. τc = 8 N/mm²
  Usually not required for smooth circular and oval profiles
Verifications and proofs

## Slide 28: Stability
The stability proof is a determination of the safety against buckling of rather thin-walled structures such as liner
Critical pressure
Buckling factor
Liner stiffness
Reduction factor
Verifications and proofs

## Slide 29: Inner pressure, temperature
Barlow's formula
  Normal force only
Temperature
  Consideration of warming and cooling down
  Additional gap occurs at further cooldown
  Mechanical properties of plastic liner are temperature dependant
Verifications and proofs

## Slide 30: Deformations
Serviceability verification
  Partial safety factors γF = γM = 1
Total deformation δv ≤ 10%
  (elastic + imperfections), guide value
Elastic deformations are limited
  δv,el ≤ 3% for water pressure
  δv,el ≤ 6% for earth and traffic loads
  δv,el ≤ 2% or 10 mm for railway loads (DB)
Verifications and proofs

## Slide 31: Soil limit stress
The sum of lateral earth pressure and bedding reaction pressure must not exceed max qh
Relevant when high lateral bedding forces are required for system stabilization
  for traffic loads with shallow installations e.g.
Should prevent soil fracture in the pipe springlines
Verifications and proofs

## Slide 32: Stress in the host pipe (HPC II and III)
Compression transmission in the springline joint must be proven in HPC III
In HPC II the proof is optional
Parabolic stress flow on bD
If the proof is not fulfilled -> HPC IIIa
Verifications and proofs

## Slide 33: Fatigue proof
Required for
  Road traffic: LM1 earth cover < 1,5 m (calculated for LM 3 – lighter model)
  Railway traffic: LM71 earth cover < 5,5 m
  Airplane: BFZ
Manufacturer must determine the amplitude (time consuming tests)
  LM71 with 108 cycles
  LM71, side tracks with 5x106 cycles
  BFZ, LM1: number of cycles not defined
Verifications and proofs

## Slide 34
IngSoft

## Slide 35: Static-Software IngSoft EasyPipe
  A127 buried pipes in trench or dam
  A161 jacking pipes
  M127-2 lining according to the global safety approach, replaced by
  A143-2 lining according to the semi-probabilistic safety approach
  M 45 buried GRP pipes (USA)
  SIA 190 buried pipes (Switzerland)
  Manhole (currently EasySchacht98) DWA-M 127-4 pending
  Extensions (special vehicles, profile from drawing, pipe with base, egg-shaped cross-section in HPC III in last stage of development)
IngSoft

## Slide 36: A143-2 with Extension Egg-Shaped Profiles in HPC III
Extension available for the modules M127-2 and A143-2
Until now, the approximation method mentioned in the set of rules made use of a substituted circle. This approach is sometimes on the unsafe side.
Egg profile in HPC III takes the actual geometry into account and incorporates it into a regular-shaped framework model
IngSoft

## Slide 37: Engineer Services and finite element analysis (FEA)
  Customers Worldwide
  Manufacturers of Liners, Pipes and Manholes
  Engineering bureaus, institutes and universities
  Sewer and Drains Rehabilitation
  Relining for arbitrary profiles in HPC I – II – III
  Structural calculation for host pipe classification
  Wall-thickness optimization
  New Installation of Pipes, Manholes, Reservoirs
  Finite Element Analyses (FEA) for special geometry
IngSoft

## Slide 38: Vladimir Lacmanovic
IngSoft
2012 Dipl. Ing. (Univ. Belgrade) Structural Engineering
Since 2012 working at IngSoft
Responsible for
  Static Calculations
  FEM Analysis
  Software IngSoft EasyPipe (Training, Support, Distribution)

## Slide 39: Thank you for your attention
Contact
  IngSoft GmbH Irrerstraße 17 90403 Nürnberg Germany
  Tel. +49 911 430879-300
  E-mail: statik@ingsoft.de
  Internet: www.easypipe.ingsoft.com