## Slide 1
  Structural aspect of HDD installations (Horizontal Directional Drilling)
  HDD designs acc. DWA-A 161 / DVGW GW 312 at NO-DIG TÜRKIYE 2024
  Dipl.-Ing. (FH) Frederik Müller M.Eng. IngSoft GmbH, Nürnberg, Germany

## Slide 2: Horizontal Directional Drilling (HDD)
Introduction

## Slide 3: Horizontal Directional Drilling (HDD)
Introduction

## Slide 4: Agenda HDD
Set of rules: DWA-A 161 / DVGW GW 312
Terms for HDD
Live-Demo: HDD Installation
Software IngSoft EasyPipe
  Calculation examples live

## Slide 5
Set of rules: DWA-A 161 / DVGW GW 312
Pipe jacking in the sense of: mining, tunnelling
(not: HDD (yet))

## Slide 6: Static Calculation of Jacking Pipes
Versions: Predecessor: edition 1990, Draft: September 2010, Released: March 2014
Correction sheets
  May 2017
  Corrections to the correction sheet in October 2017
  Corrigendum September 2020  March 2021 (due to: DWA-A127-10 material parameters)
English version May 2018 (IngSoft assisted)
Costs: 93.50- €, available at https://shop.dwa.de/en/DWA-A-161E-Static-calculation-of-Jacking-Pipes-March-2014-corrected-version-March-2021/A-161E-Hauptprodukt-14-main
Set of rules: DWA-A 161 / DVGW GW 312
Notes: A161 = GW312

## Slide 7: Overview of rules and regulations
Semi-probabilistic partial safety concept
  Actions E (loads): Increase by E * F
  Resistance R: Reduce by R / M
Verification for single pipe element
Pipe length of the individual pipe due to load approach
Bedding angle A127 <> A161
Pressure Transfer Ring (PTR): Test report!
Interaction of radial and axial direction
Iterative determination of the maximum jacking force that the individual pipe can withstand
Set of rules: DWA-A 161 / DVGW GW 312

## Slide 8: Expectations
Not covered ( e.g. DWA-A 125)
  Total length of jacking route
  Surface friction between pipe and soil
  Front face pressure, jacking stations
  Any procedure that „pulls“ the pipe, like HDD
Covered
  Single pipe element is dimensioned
  Material parameters
  Semi-probabilistic concept of partial safety coefficients by
    Multiplication of loads by γF > 1
    Division of material data by γM > 1
  Interaction of radial and axial direction
  Installation and operational state
Set of rules: DWA-A 161 / DVGW GW 312
https://ars.els-cdn.com/content/image/1-s2.0-S2467967418301065-gr1_lrg.jpg

## Slide 11: Loads (Actions)
Dead weight of pipe, soil
Street
  Load Model 1, LM1 (instead! of SLW60/HGV60)
  Cover height at least 1.0 m
  Fatigue proof: 2x10^6 load cycles
Railway
  Load Model 71, LM71
  Impact coefficient
  Cover height: 1.10 m
  Fatigue proof: 1x10^8 load cycles (instead of 2x10^6)
  For steel pipes: 5x10^6 possible, but 1x10^8 required if cover depth < 1.5 m, acc. EuroCode 3, EC3
Optional: ground water, inner pressure
Set of rules: DWA-A 161 / DVGW GW 312

## Slide 12: Pipe jacking
Radial and longitudinal actions
Procedures
  "Classical" procedure (mining, tunnelling)
  Pilot pipe
  Soil displacement, burst lining
Pressure Transfer Ring (PTR)
Set of rules: DWA-A 161 / DVGW GW 312

## Slide 13: Pressure Transfer Ring (PTR)
Wooden ring
Axial stress distribution between single pipe elements
Picture 1 From ATV-A 161 (1990)
Picture 2 From DWA-A 161 (2014)
GRP in EasyPipe: no PTR
Set of rules: DWA-A 161 / DVGW GW 312

## Slide 14: Special feature for jacking in mixed soils
DWA-A 161, section 8
Jacking partly in rock, partly in loose soil
Mixed soils (Fig. 9) are unfavourable for the pipe
Set of rules: DWA-A 161 / DVGW GW 312
Loose soil
Solid rock
Mixed soil

## Slide 15: Special feature of jacking completely in solid rock
Reduce cover depth if necessary
Coordination with the geotechnical expert
Minimum value: two times outer diameter 2 x DA (8.2.2)
Set of rules: DWA-A 161 / DVGW GW 312
Soild rock
ex. hü
red. hü > 2DA
pV

## Slide 16: Required verifications
Set of rules: DWA-A 161 / DVGW GW 312

## Slide 17: Minimum wall thickness
Set of rules: DWA-A 161 / DVGW GW 312
Why are there minimum wall thicknesses/reinforcement?
  Compensation of axial/radial stress interaction
  Avoidance of sudden failure
Minimum wall thicknesses
  Independent of the actions ("loads")
  Independent of the installation conditions
  Dependent on the material (Tables 19, 20)
  Reinforced concrete pipes -> DIN V 1201, 5.3.5.2: t/rm = 0.17
  Depending on the nominal diameter DN
Minimum reinforcement
  Section 9.3.2 ->DIN V 1201, 5.3.7
  0.7% of the minimum wall thickness required

## Slide 18: Minimum sectional forces
Set of rules: DWA-A 161 / DVGW GW 312

## Slide 19: Equivalent stresses
Set of rules: DWA-A 161 / DVGW GW 312
Interaktion
  Radial & axial direction overlay
  Construction state
Determination of the maximum permissible jacking force

## Slide 20: Approval
Earth, groundwater, inner pressure, traffic loads
  Verifications for stresses/strains, deformations (circumferential)
  Buckling/stability for steel, GRP, plastic pipes
Construction state
  Pulling force: Tension
  Curvature: Bending
  Interaction of tension and bending (longitudinal)
  Lubricant pressure
Operational state
  Bending from installation “remains”
  Service life of 50 years (and more): Long-term material characteristics for time-dependent materials, fatigue check for live loads
Set of rules: DWA-A 161 / DVGW GW 312

## Slide 21: Tensile force, axial stresses: DCA Technical Guidelines
Longitudinal tensile force from retraction
  Approach DCA: full length drawn
  Coefficient of friction
  Result: required tensile force
Longitudinal tensile force permissible
  "Endless" pipe string (e.g. PE, steel)
  Permissible stress of pipe material x ring surface
  Result: permissible tensile force
Axial forces (or stresses): verification
Consider partial safety factors
Reductions, if necessary
Set of rules
Notes: ### ab 2. Punkt, this is where DCA ends
(Single pipes: Verification of socket e.g. with BLS, duktus)

## Slide 22
Terms for Horizontal Directional Drilling (HDD)

## Slide 23: Tensile force, tensile stress
Terms
Fibres are pulled
Applies to all fibres
No relocations possible
Sign positive (+) for stresses
Notes: ### Schnur ziehen

## Slide 24: Bending moment, bending stress
Terms
Fibres are
  Compressed (50%)
  Pulled (50%)
Centric neutral fibre
Outermost fibres get
  Maximum compression
  Maximum tension
Relocations possible
Sign for stresses
  Negative if compressed (-)
  Positive if pulled (+)
Notes: ### Rohrstück biegen

## Slide 25: Interaction, superposition
Terms
Stress blocks superimposed
Neutral fibre shifted
Tensile + bending stresses

## Slide 26
Live demonstration

## Slide 27: Transportation Nürnberg - Istanbul
Live demonstration

## Slide 28: Construction state
Live demonstration
Equipment from my basement
You 
Notes: ### THREE volunteers required
### someone take a picture (please)

## Slide 29: Construction state
Live demonstration
Rig  Pull Pipe

## Slide 30: HDD – Horizontal Directional Drilling
Live demonstration

## Slide 31
Software IngSoft EasyPipe

## Slide 32: Structure of the program surface
IngSoft EasyPipe
Results
Entry
Statics structure
Help / Sketch
Menu / Print / Units / Languages

## Slide 33: Context-sensitive help
Instead of a manual
or each chapter
For each entry
If necessary with sketches
IngSoft EasyPipe

## Slide 34: Languages and Units (Professional Edition)
Switching between languages while working
Please note: English language setting uses Point . (1.0) instead of Comma , (1,0)
Switching between metric and imperial units while working
IngSoft EasyPipe

## Slide 35: Databases (Professional Edition)
Solid and corrugated pipes incl. material
GRP pipes for A127 and A161
Reinforced concrete
Literature reference
Path to a central server
Installation folder EasyPipe will be overwritten after the update
IngSoft EasyPipe

## Slide 36: Alternatives (Professional Edition)
All entries are inherited from the source calculation
Overall changes are made in the source calculation
Individual changes are made in the alternative calculation
Build cascading projects
IngSoft EasyPipe

## Slide 37: External attachments: .pdf and .jpg
As a link, missing in the IngSoftEasyPipe project file (.epn) If necessary, send attachment separatelyIs
always printed, regardless of the length of the printout
Header/footer uniform
Warning if the path has changed or been deleted
IngSoft EasyPipe

## Slide 38
LIVE-DEMO
IngSoft EasyPipe

## Slide 39: Consistent software solution
Advertisement

## Slide 40: Frederik Müller
IngSoft
Department Manager Structural Analysis, Authorized Signatory
  Graduate Engineer (FH) Civil Engineering, Master of Software-Engineering (M.Eng.)
  Employed by IngSoft since 2010
  Main focus: Sales, Support ATV-DVWK-A 127, DWA-A 161

## Slide 41: Thank you for your attention
Contact
  IngSoft GmbH Irrerstraße 17 90403 Nürnberg Germany
  Tel: +49 911 430879-300
  E-Mail: statik@ingsoft.de
Internet: www.easypipe.ingsoft.com